## Slide 1: Status of the BRAMS network
H. Lamy
BRAMS Annual Meeting
Grimbergen, 30/05/2026

## Slide 2: BRAMS receiving stations
4 stations with ICOM left : BEOTTI, BEKAMP, BEGRIM, BEREDU
7 Boxes with Rock 4SE instead of Rpi : BEHARE, BELANG, BEGENT, BESIVR, BELIEG, BELEUZ, FRMAUB
2 stations with very poor SNR : BEOOSE, BEMAAM
52 stations

## Slide 3: New remote control and data transfer
Reverse ssh is used for both data transfer and remote control
This replaces respectively transfer to our web server (brams_communicator) and Hamachi

## Slide 4: One new interferometer in Ecotron
Excellent site in terms of SNR

## Slide 5: One new interferometer in Ecotron

## Slide 6: One new interferometer in Ecotron

## Slide 7: One new interferometer in Ecotron
One Master Box
One Distribution box (Calibrateur, GPSDO for 24 MHz reference, GPS for 1PPS+NMEA)

## Slide 8: Lessons learnt from interferometer in Humain
Use of gutters  easier to install and possibly replace the coaxial cables
Center phases of antennas at same height (within 1-2 cm)
Matching elements of antennas protected with self-fusing tape  no problem with intensity of the calibrator signal
Linux, no more Windows  better stability
Better stability of the sampling frequency (previous sampler in Humain was not controlled by an external frequency reference)
Additional difficulty : sampling is made independently for each Rx and controlled by different Rpi  lack of synchronicity due to various states of OS on the Rpis  solution : modified calibrator (see talk by Michel)

## Slide 9: New stations
Lonzée (near Gembloux)
Loupoigne (near Genappes)
Havelange (near Marche-en-Famenne)
Durbuy
Bocholt
Candidates?

## Slide 10: Second transmitter?
Idea : have a second Tx transmitting 2 KHz above the current beacon such that meteor echoes will appear around 1 KHz for BRAMS beacon 1 and 2 KHz for BRAMS beacon 2
Double number of pairs Tx-Rx
Location : not much has been done  contact with SCK-CEN, TABLOO …. But nothing concrete yet
Any suggestion?

## Slide 11: Projects
SORBET  Ending in 2026
PhD Hugo Joly  until December 2029
MAMBO (Mass and ionisAtion of Meteoroids from BRAMS observations)  P4S Call  not selected
MIMBO (Mass and Ionisation of Meteoroids from BRAMS observations)  FNRS call  answer around mid-June  if not selected, the candidate Zara Zaman (CAN) will present a similar project at FRIA later this year
INTERCEPTOR ( sIgNaTure of hypERsoniC objEcts: dual aPplicaTiOn of fiReballs, VKI leads)  DEFRA call  answer by mid-September
STCE (Solar Terrestrial Center of Excellence)