## Slide 1: BRAMS : advances on Trajectory retrieval
  Content
Initial state and limitations
Current advances
Future work
Notes: 1

## Slide 2
First a few definitions :
L0 - Data collection
Shifting to audio domain
Sampling signal
Determining timestamps
Storing data
L1 – Extracting measured quantites
Filtering parasitic signals (beacon, airplanes)
Detecting echoes
Determining T0,speed,…
L2 – « Trajectory Retrieval »
Inferring meteor trajectory from measurements
Inverse problem => Iterative scheme
Orbit determination
L3 – Large-scale processing
Autonomous retrieval
Meteor counts
Shower activities
…
Notes: 2

## Slide 3: First task : further optical validation
Poor results…
Very few events yield enough echoes
Solver (L2) crashes
Nonphysical solutions
Notes: 3

## Slide 4: Limitations :
Notes: 4

## Slide 5
Manual counts at Ecotron for 1 hour
=> 192 echoes detected
=> 70 were successfully characterised
=> 48 groups with 6 echoes or more
=> 20 of which only have ToF
=> 10 Trajectories with more than 2 PreT0
=> Outlier filtering, spurious data
=> Only 6 viable trajectories !
Limitations : L1
Notes: 5

## Slide 6
Manual counts at Ecotron for 1 hour
=> 192 echoes detected
=> 70 were successfully characterised
=> 48 groups with 6 echoes or more
=> 20 of which only have ToF
=> 10 Trajectories with more than 2 PreT0
=> Outlier filtering, spurious data
=> Only 6 viable trajectories !
Limitations : L1
Notes: 6

## Slide 7
ToF-PreT0 incompatibility
Limitations : L1
 | Underdense | Trans/Overdense
ToF | Works well | Rejection due to shape criteria ; Poor handling of fragmentation
Pre-T0 phase | SNR too low | Works well
Very narrow sweetspot !
Notes: 7

## Slide 8
Poor fragmentation/overdense handling
Limitations : L1
Notes: 8

## Slide 9
Limitations : L1
Airplane substraction
Notes: 9

## Slide 10
Limitations : L1
Airplane substraction
Notes: 10

## Slide 11
Limitations : L1
Airplane substraction
Notes: 11

## Slide 12
Limitations : L1
« Punches a hole» in the spectra of echoes
Loss of energy
Distorted shape
Notes: 12

## Slide 13
Limitations : L1
Poorly estimated SNR & Uncertainties
Good measurements are ignored => Loss information
Noisy measurements are given too much importance
=> Deterioration of the fit
Notes: 13

## Slide 14
Limitations :
How to determine whether two echoes belong to the same event ?
Fragmentation
Spurious data
Simultaneous events
L1.5 ?
Notes: 14

## Slide 15: Limitations :
Slow (± min/call)
Unstable
Rigid structure : Hard to implement new features (deceleration, new meas. types…)
Notes: 15

## Slide 16: Current progress :
Notes: 16

## Slide 17: Solver (L2) :
Complete rewrite(s) of the L2 algorithm :
Fully custom iterative scheme
More stable
Massive Speed-up : ±45s -> ±150ms
Multi-emitter support
Fully modular
Notes: 17

## Slide 18: Solver (L2) :
Example of modularity : Implementation of ToF
L1
?
Trajectory
Geometry
Model
Kinematic Model
Notes: 18

## Slide 19: Selector (L1.5) :
Notes: 19

## Slide 20: Echo characterization (L1) :
New airplane filtering technique (Early WIP)
New echo analysis techniques (Under investigation)
Goals :
  Speed-up (>>50min of data/min)
  Detect and analyze every echo
Notes: 20

## Slide 21: Airplane substraction (L1) :
Notes: 21

## Slide 22
Limitations : L1
Airplane substraction
Notes: 22

## Slide 23
Limitations : L1
Airplane substraction
Notes: 23

## Slide 24: Airplane substraction (L1) :
Notes: 24

## Slide 25: Airplane substraction (L1) :
Notes: 25

## Slide 26: Airplane substraction (L1) :
Notes: 26

## Slide 27: Airplane substraction (L1) :
Notes: 27

## Slide 28: Airplane substraction (L1) :
Notes: 28

## Slide 29: Airplane substraction (L1) :
Notes: 29

## Slide 30: Airplane substraction (L1) :
Notes: 30

## Slide 31: Airplane substraction (L1) :
Notes: 31

## Slide 32: What next ?
Orbit determination
Plot utilities
Autonomous retrieval